## Slide 1: [QA] – SMAC Ubuntu RF tool User Guide (SV6158_24M XTAL)
QA 2020-12-23

## Slide 2: SMAC Ubuntu RF tool User Guide
1. 版本編譯
2. RF tool 操作指令
  RF tool tx
  Rate table
  RF tool rx

## Slide 3: 版本編譯
  版本: L.SMAC.20Q2.r7290
  Build code
    cd ssv6x5x
    ./unload.sh
    make clean
    make
    make install

## Slide 4: Ubuntu相關環境設定
  1. 關閉Ubuntu內建Wifi GUI
  (避免主動scan的行為)
    service network-manager stop
  2. Load Driver and Enable Interface
    ./unload.sh
    ./load.sh
    rfkill unblock wifi
    ifconfig wlanX up
  3. Notice item:
  此rf tool使用過後若需繼續操作正常連線請 重新上電並reload driver

## Slide 5: RF tool
RF tool tx(執行步驟如下, 每個指令每次需都執行)
  停止rf tx/rx
    ./cli rf stop
  設定rf tx channel
    HT20 or non-HT : ./cli rf ch 6
    HT40: ./cli rf ch 6 bw40
  設定rf tx rate(rate table請參考下一頁)
    ./cli rf rate 22
  開始rf tx(後面數字代表interval, 單位us)
    ./cli rf tx 1
    ./cli rf tx (不打數字代表continuous mode)

## Slide 6: RF tool
Rate table
Rate n pattern format | Rate n pattern format
0 = 11b 1M | 7 = NON-HT 6M
1 = 11b 2M | 8 = NON-HT 9M
2 = 11b 5.5M | 9 = NON-HT 12M
3 = 11b 11M | 10 = NON-HT 18M
4 = 11b 2M SP | 11 = NON-HT 24M
5 = 11b 5.5M SP | 12 = NON-HT 36M
6 = 11b 11M SP | 13 = NON-HT 48M
 | 14 = NON-HT 54M

## Slide 7: RF tool
Rate n pattern format | Rate n pattern format
15 = HT-MM MCS0 | 31 = HT40-Mcs0
16 = HT-MM MCS1 | 32 = HT40-Mcs1
17 = HT-MM MCS2 | 33 = HT40-Mcs2
18 = HT-MM MCS3 | 34 = HT40-Mcs3
19 = HT-MM MCS4 | 35 = HT40-Mcs4
20 = HT-MM MCS5 | 36 = HT40-Mcs5
21 = HT-MM MCS6 | 37 = HT40-Mcs6
22 = HT-MM MCS7 | 38 = HT40-Mcs7

## Slide 8: RF tool
RF tool rx(執行步驟如下, 每個指令每次需都執行)
  停止rf tx/rx
    ./cli rf stop
  切換至rf rx
    ./cli rf rx
  設定rf rx channel
    ./cli rf ch 6
  Reset rf rx
    ./cli rf rxreset
  讀rf rx packet count
    B mode: ./cli rf count 1
    G/N mode: ./cli rf count 2

## Slide 9: 谢谢 Thank You